## Slide 1: Hybrid RRAM-NEM Relay Design for Nonvolatile 3D Routing in CGRAs
Akash Levy

## Slide 2: Designing an application today
Code
CUDA
RTL/HLS
RTL + PNR + Tapeout
CGRA
CGRA*
CGRA
Source: https://hackernoon.com/a-gentle-introduction-to-hardware-accelerated-data-processing-81ac79c2105
* Workload-dependent
Design Flow:
Notes: Today we have many options for designing an application. Here’s a diagram showing the supposed tradeoffs between different application design flows.
Flexibility = What applications can be run on it
Efficiency = EDP
Cost per unit = NRE cost
We have CPUs which you run software on, GPUs which you run CUDA software on, FPGAs which you compile RTL to (or use HLS), and ASICs which have the most complex design flow.
More recently, we also have CGRAs, which are coarse-grained FPGAs, meaning they replace some LUTs with common logic structures. These have a somewhat interesting profile on this scale.
CGRAs are FPGAs that tradeoff a small amount of flexibility for a decent amount of efficiency (depending on workload though)
Same design flow should mean same cost per unit

## Slide 3: Where does reconfigurability overhead come from?
LUTs are less efficient than standard cells
  Increase area
  Increases power and delay a little
  Less of a problem for CGRAs: use more efficient logic blocks
Unutilized logic components
  Increase area
  Less of a problem for FPGAs: homogeneity within CLBs
Reconfigurable Routing
  Increases area (80-90% of FPGA area is routing)
  Increases power (5-12x)
  Increases delay (3-4x)
Notes: So we need to think about what causes this overhead. There are three main causes.

## Slide 4: Reducing reconfigurable routing overhead using emerging nanotechnologies
NEM relays:
  Reconfigurable switches monolithically integrated in 3D
  Reduce area/power/delay overhead from reconfigurable interconnects
RRAM:
  Non-volatile memory monolithically integrated in 3D
  Reduce area/power/delay overhead from startup configuration
Result:
  Lower routing overhead
  No startup reconfiguration cost
Notes: Result:
CGRAs become competitive with ASICs in terms of performance
CGRAs become competitive with ASICs for “normally off, instantly on”

## Slide 5: Combining RRAM and NEMS approaches
RRAM and NEM relays have been separately studied for FPGAs
So what is really novel about combining approaches?
KEY POINT: If used together, the electrical properties of RRAM and NEM relays complement each other to cancel essentially all overhead

## Slide 6: NEM Relays
What are they and how do they work?

## Slide 7
Beam
Source
Drain
Gate
Source
Drain
Gate
Beam
Electrostatic
force
Vpo
Vpi
Vhold
VGS
IDS
Hysteresis Window
Infinite subthreshold slope
3-terminal (3T) NEM relay
OFF-state
ON-state
(VB = VS)

## Slide 8: 3T & 4T NEM Relays
Source: C. Chen, R. Parsa, N. Patil, S. Chong, K. Akarvardar, J. Provine, D. Lewis, J. Watt, R. T. Howe, H.-S. P. Wong, et al., “Efficient FPGAs using nanoelectromechanical relays,” in Proceedings of the 18th annual ACM/SIGDA international symposium on Field programmable gate arrays, pp. 273–282, ACM, 2010.

## Slide 9: Modern Clamped-Clamped 4T NEM Relay
Source: Ye, Z. A., S. Almeida, M. Rusch, A. Perlas, W. Zhang, U. Sikder, J. Jeon, V. Stojanović, and T-JK Liu. "Demonstration of 50-mV Digital Integrated Circuits with Microelectromechanical Relays." In 2018 IEEE International Electron Devices Meeting (IEDM), pp. 4-1. IEEE, 2018.

## Slide 10: New idea: multi-bit routing with NEM relays
CGRAs have multi-bit signals that need to be routed
Why not route multiple bits with a single NEM relay to save area?
Already done with two bits, want to test limits of bit-width scalability
Bit 1
Bit 2

## Slide 11: Previous work on NEM relays for FPGAs
C. Chen, W. S. Lee, R. Parsa, S. Chong, J. Provine, J. Watt, R. T. Howe, H.-S. P. Wong, and S. Mitra, “Nano-electro-mechanical relays for FPGA routing: Experimental demonstration and a design technique,” in Design, Automation & Test in Europe Conference & Exhibition (DATE), 2012, pp. 1361–1366, IEEE, 2012.
  3D place-and-route scheme with NEM-based LUTs and routers
  Maximum of 41.9% performance gain
C. Chen, R. Parsa, N. Patil, S. Chong, K. Akarvardar, J. Provine, D. Lewis, J. Watt, R. T. Howe, H.-S. P. Wong, et al., “Efficient FPGAs using nanoelectromechanical relays,” in Proceedings of the 18th annual ACM/SIGDA international symposium on Field programmable gate arrays, pp. 273–282, ACM, 2010.
  Half-select programming scheme was used for the NEM relays, verified expt.
  43.6% footprint area reduction, 37% leakage power reduction, and up to 28% critical path delay reduction
Both papers used somewhat optimistic device parameters/dimensions that have not been physically realized yet

## Slide 12: Half-Select Design for NEM Relay R/W
Source: C. Chen, R. Parsa, N. Patil, S. Chong, K. Akarvardar, J. Provine, D. Lewis, J. Watt, R. T. Howe, H.-S. P. Wong, et al., “Efficient FPGAs using nanoelectromechanical relays,” in Proceedings of the 18th annual ACM/SIGDA international symposium on Field programmable gate arrays, pp. 273–282, ACM, 2010.

## Slide 13: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties |  | 
Infinite subthreshold slope | Storage is volatile |  | 
Lower ON-state resistance than transistors | Larger than transistors |  | 
Hysteresis enables data storage | Much slower switching than transistors |  | 
3D integration | Higher Vg req. than CMOS |  | 
No leakage current |  |  | 

## Slide 14: RRAM
What is it and how does it work?

## Slide 15
Bottom Electrode
Resistive Switching Film
Top Electrode
=
Bipolar RRAM Cell
Hysteresis in resistance
Many possible materials for resistive switching film
Many possible R/W circuit architectures
Key properties:
  Endurance
  Retention
  Max DC current/voltage
  LRS, HRS, resistance ratio
  DC peak voltage
Publication & Year | VLSI 2014 | VLSI 2014 | IEDM 2014 | IEDM 2014 | VLSI 2015 | VLSI 2015
2D/3D Geometry | 2D Planar | 3D Vertical | 2D Planar | 3D Vertical | 2D Planar | 2D Planar
Switch Type | Bi | Bi | Bi | Bi | N/A | Bi
Structure | 1T-1R | 1R | 1T-1R | 1R | 1T-1R | 1R
TE/material/BE | Al/AlOx/WOx/W | TiN/HfOx/TiN | TiN/Ti/HfO2/TiN | Pt/HfOx/TiN | Ir/Ta2O5/TaOx/TaN | TiN/TiO2/a-Si/TiN
Cell Area (μm2) | 0.0324 (.18um) | 0.000003 | 0.01 (100nm) | 1 (15nm) | 0.0016(40nm) | 0.0013
Speed [ns] | ~1000 | 50 | 40 | 20 | N/A | 10
DC Peak Voltage [V] | N/A | <3 | <3 | <2.5 | N/A | 6.5
DC Peak Current [uA] | N/A | ~500 | ~60 | ~100 | N/A | 5
HRS/LRS Ratio | >180 | >10 | 10 | 100 | 10 | 10
R high [Ω] | 3x107 | 106 | 2x105 | 3x107 | 5x104 | 108
R low [Ω] | 3x104 | 104 | 2x104 | 3x104 | 4x103 | 107
Endurance | 109 | 104 | 103 | 108 | >105 | 106
Retention | 10y@ 85℃ | 20000h@ 250℃ | 10y@ 70℃ | 10y@ RT | 10y @ 85℃ | 3y @ 55℃
VRESET
VSET
V
I
SET
HRS
LRS
RESET
Compliance

## Slide 16: Previous work on RRAM for FPGAs
Y. Y. Liauw, Z. Zhang, W. Kim, A. El Gamal, and S. S. Wong, “Nonvolatile 3D-FPGA with monolithically stacked RRAM-based configuration memory,” in Solid-State Circuits Conference Digest of Technical Papers (ISSCC), 2012 IEEE International, pp. 406–408, IEEE, 2012.
  1T2R structure with two RRAM cells having opposite resistance states
  Voltage divider controlling a pass transistor
  Experimentally achieved a 57% smaller die area and a 28% lower energy-delay-product (EDP) than SRAM-based design
  Non-volatile configuration memory which enabled quick wake-up
Possible problems:
Leakage through RRAM during operation
Endurance/retention

## Slide 17: RRAM 1T2R Operation Modes

## Slide 18: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties | Good properties | Bad properties
Infinite subthreshold slope | Storage is volatile | Nonvolatile | Large write energy
Lower ON-state resistance than transistors | Larger than transistors | Lower area than SRAM and proven scalable | Sense amp to decode takes up area
Hysteresis enables data storage | Much slower switching than transistors | Resistance-based storage allows analog design | 
3D integration | Higher Vg req. than CMOS | 3D integration | 
No leakage current |  |  | 

## Slide 19: How can we synergize RRAM & NEM relays?
KEY IDEA: use RRAM to control gate voltage of NEM relays for actuation
More generally: NEM relays are an interesting option for RRAM sense amplification, given their infinite subthreshold slope
NEM relays have better electrical characteristics than pass transistors

## Slide 20: Hybrid Circuit Architecture
Mode | Param | Value
COPY (global) | Vrow,C | 
 | Vcol,C | 
HOLD (global) | Vrow,H | 
 | Vcol,H | 
SET | Vrow | Step 1: Step 2:
 | Vcol | 
RESET | Same voltages as SET mode, but switch Vrow and Vcol | 
Mode | Param | Value
COPY (global) | Vrow,C | 
 | Vcol,C | 
HOLD (global) | Vrow,H | 
 | Vcol,H | 
SET | Vrow | 
 | Vcol | 
RESET | Same voltages as SET mode, but switch Vrow and Vcol | 
(b)
(a)
out
Vg
Vcol,1
Vcol,2
src1,1
src1,2
src2,1
src2,2
Vrow,1
Vrow,2
drn1,1
drn1,2
drn2,1
drn2,2
Hysteretic 4T NEM Router
RRAM Cell
Vg
-
+
+
-
Notes: Key idea: use RRAM to actuate the NEM relays
Entirely back-end-of-line (0T)
1N1R design
Need a good way to actuate
Poly layers are annoying to get to
RRAM properties have to match NEM relays’

## Slide 21: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties | Good properties | Bad properties
Infinite subthreshold slope | Storage is volatile | Nonvolatile | Large write energy
Lower ON-state resistance than transistors | Larger than transistors | Lower area than SRAM and proven scalable | Sense amp to decode takes up area
Hysteresis enables data storage | Much slower switching than transistors | Resistance-based storage allows analog design | 
3D integration | Higher Vg req. than CMOS | 3D integration | 
No leakage current |  |  | 
Bad Material Property | Good Material/App Property that Cancels It
NEM relays: much slower switching than transistors | Used for routing only: only switches once on startup, hysteresis enables dual function as memory and router
NEM relays: larger than transistors | Used for routing only and integrated in 3D
NEM relays: storage using hysteresis is volatile | RRAM is nonvolatile: integration enables nonvolatility
NEM relays: higher Vg required than CMOS | RRAM variable resistance allows analog control of Vg
RRAM: larger write energy | RRAM is used as ROM
RRAM: sense amp to decode takes up area | NEM relays have infinite subthreshold slope, so single relay can act as decoder
RESULT: Architecture is entirely free of transistors, so can be implemented 100% in BEOL i.e. 3D

## Slide 22: Preliminary SPICE Simulations
Using simplest RRAM+NEM relay HSPICE models
  Lumped models written in Verilog-A
  Abrupt switching behavior (pretty unrealistic)
  Not accounting for device variability, nonlinear effects, etc.
Tested all possible valid state transitions with time trace
Tested with small crossbar array (3x3)
Future work: use more accurate models

## Slide 23: Valid state transitions
out
Vg
Vcol,1
Vcol,2
src1,1
src1,2
src2,1
src2,2
Vrow,1
Vrow,2
drn1,1
drn1,2
drn2,1
drn2,2
Hysteretic 4T NEM Router
RRAM Cell
Vg
-
+
+
-

## Slide 24: Time trace of valid state transitions in HSPICE
OFF_0
SET
OFF_1
COPY_1
HOLD_1
OFF_1
RESET
OFF_0
COPY_0
HOLD_0
OFF_0
MODE:

## Slide 25: Half-select problem
Avoiding write disturbance requires RRAM to have asymmetric SET/RESET voltages
Approximately speaking:
|VSET| > |VRST|

## Slide 26: Row/col controllers
https://www.falstad.com/circuit/circuitjs.html
Notes: (single stream for reduced I/O pin requirement)
Probably want to do this on-chip to reduce pin requirement
Column controller is similar

## Slide 27: Island-Style Architecture
CB
PE
CB
SB
One CGRA Tile
Source: FPGA Architectures: An Overview - Springer
Notes: CLB: configurable logic block
CB: connection box
SB: switch box

## Slide 28: RRAM/NEMS switch layouts
NEM
Relay
Anchor
NEM
Relay
Anchor
NEM
Body
Channel
Gate line (M9)
Gate body
S/D contact
Vias
RRAM
RRAM
Row line (M8)
Column line (M7)
4T
Image generated with GDS3D
Gnd Pin for Anchor
Dimple

## Slide 29: RRAM/NEMS switch layouts (~5um x 5um)
Custom technology based on SAED32 PDK. 5 new layers added: RRAM (between M8/M9), NEMDIMP, NEMANC, NEMCHAN, NEMBEAM
Notes: TODO: add measurements on critical dimensions

## Slide 30: PE Tile Layouts (~90um x 90um)
View from Synopsys IC Compiler
GDSII stream-out loaded into Cadence Virtuoso

## Slide 31: Switch boxes
Source: http://venividiwiki.ee.virginia.edu/mediawiki/index.php/File:SwitchBo.png
Flexibility: Fs = 3

## Slide 32: Connection boxes
PE
PE
Fc = 0.5

## Slide 33: Layout strategy: 3D stacking of CBs + SBs
CB
PE
CB
SB
CB
PE
CB
SB
CB
PE
CB
SB
CB
PE
CB
SB
PE
PE
SB + 2 CBs
SB + 2 CBs
CBs and SBs will be laid out using crossbar tiling of stdcells
PE will then be routed to pins in upper metal layers
Notes: Need to get to 1/3 area for full utilization

## Slide 34: (Future Work: LUTs with RRAM/NEMS)
Source: FPGA Architectures: An Overview - Springer
Key idea: replace SRAM with RRAM/NEMS but leave muxes in CMOS for speed
Notes: Ultimately you want all static configuration to use this architecture

## Slide 35: Next Steps
Simulation & Modeling
Test with different device parameters
Test with different device models with varying levels of sophistication
Simulate NEM relay behavior using FEA tool
Optimize shape of NEM relays using FEA tool
Predict NEM relay stiction and contact resistance
More advanced NEM relay model: calibrate to experimental data too
VLSI Design
Make standard cells with different bit widths and estimate properties (Vpo, Vpo, endurance, etc.)
PnR to build switch boxes and connections boxes
Architectural analysis w/fully laid out blocks
Architectural Analysis
Calculate approximately what benefits are (area, energy, delay)
Build a parametrized cost model for system components (average area/energy/delay cost, given switch box parameters, size of array, etc.)
Fabrication & Characterization
Test dual-RRAM SET/RESET and voltage divider properties
Test crossbar array of dual-RRAM SET/RESET and voltage divider properties
Fabricate NEM relays with larger bit widths
Integration with AHA CGRA
Row/column drivers need to be simulated
Predict NEM relay pull-in/pull-out voltages using models
Row/column drivers need to be implemented

## Slide 36: Summary
RRAM and NEM relays work well together for reconfigurable routing
100% BEOL design enables isolation of layout for routing and logic
That’s all, folks!
Area Improvements | Power Improvements | Delay Improvements
Routing components in 3D | Lower ON-state resistance | Lower ON-state resistance
Routing components require fewer elements | Low-power startup with integrated NVM | Fast startup with integrated NVM
No config registers/SRAM | Shorter wire lengths | Shorter wire lengths
 | No leakage current |