## Slide 1: Hybrid RRAM-NEMS Design for Nonvolatile 3D Routing in CGRAs
Akash Levy

## Slide 2: Biggest problem with FPGAs/CGRAs today?
Gap between power/area/performance of FPGAs
LUTs are less efficient than standard cells
  Increase area, power, and delay
  Less of a problem for CGRAs: fewer LUTs
Unutilized logic components
  Increase area
  Less of a problem for FPGAs: homogeneity within CLBs
Reconfigurable Routing
  Increases area (80-90% of FPGA area is routing!!!)
  Increases power (5-12x)
  Increases delay (3-4x)
Notes: Flexibility = agility
Cool… assuming above is true, is that it?
What else can we do? Well basically we want to find a way to reduce reconfigurability overhead.

## Slide 3: Reducing reconfigurable routing overhead using emerging nanotechnologies
NEM relays:
  Reconfigurable switches monolithically integrated in 3D
  Reduce area/power/delay overhead from reconfigurable interconnects
RRAM:
  Non-volatile memory monolithically integrated in 3D
  Reduce area/power/delay overhead from startup configuration
Result:
  Lower routing overhead
  No startup reconfiguration cost
Notes: Result:
CGRAs become competitive with ASICs in terms of performance
CGRAs become competitive with ASICs for “normally off, instantly on”

## Slide 4
Beam
Source
Drain
Gate
Source
Drain
Gate
Beam
Electrostatic
force
Vpo
Vpi
Vhold
VGS
IDS
Hysteresis Window
Infinite subthreshold slope
3-terminal (3T) NEM relay
OFF-state
ON-state

## Slide 5: 3T & 4T Devices

## Slide 6
Bottom Electrode
Resistive Switching Film
Top Electrode
=
Bipolar RRAM Cell
Many possible materials for resistive switching film
Many possible R/W circuit architectures
Key properties:
  Endurance
  Retention
  Max DC current/voltage
  LRS, HRS, resistance ratio
  DC peak voltage
Publication & Year | VLSI 2014 | VLSI 2014 | IEDM 2014 | IEDM 2014 | VLSI 2015 | VLSI 2015
2D/3D Geometry | 2D Planar | 3D Vertical | 2D Planar | 3D Vertical | 2D Planar | 2D Planar
Switch Type | Bi | Bi | Bi | Bi | N/A | Bi
Structure | 1T-1R | 1R | 1T-1R | 1R | 1T-1R | 1R
TE/material/BE | Al/AlOx/WOx/W | TiN/HfOx/TiN | TiN/Ti/HfO2/TiN | Pt/HfOx/TiN | Ir/Ta2O5/TaOx/TaN | TiN/TiO2/a-Si/TiN
Cell Area (μm2) | 0.0324 (.18um) | 0.000003 | 0.01 (100nm) | 1 (15nm) | 0.0016(40nm) | 0.0013
Speed [ns] | ~1000 | 50 | 40 | 20 | N/A | 10
DC Peak Voltage [V] | N/A | <3 | <3 | <2.5 | N/A | 6.5
DC Peak Current [uA] | N/A | ~500 | ~60 | ~100 | N/A | 5
HRS/LRS Ratio | >180 | >10 | 10 | 100 | 10 | 10
R high [Ω] | 3x107 | 106 | 2x105 | 3x107 | 5x104 | 108
R low [Ω] | 3x104 | 104 | 2x104 | 3x104 | 4x103 | 107
Endurance | 109 | 104 | 103 | 108 | >105 | 106
Retention | 10y@ 85℃ | 20000h@ 250℃ | 10y@ 70℃ | 10y@ RT | 10y @ 85℃ | 3y @ 55℃
VRESET
VSET
V
I
SET
HRS
LRS
RESET
Compliance

## Slide 7: How can we synergize RRAM & NEM relays?
KEY IDEA: use RRAM to control gate voltage of NEM relays for actuation
NEM relays have better electrical characteristics than pass transistors

## Slide 8
out
Vg
Vcol,1
Vcol,2
in1,1
in1,2
in2,1
in2,2
Vrow,1
Vrow,2
out1,1
out1,2
out2,1
out2,2
Hysteretic 3T NEM Router
RRAM Cell
Vg
-
+
+
-

## Slide 9: RRAM/NEMS switch BEOL standard cell layout
Vcol wire (L1)
Vrow wire (L2)
Via (L2)
Vrow wire (L2)
+ Electrode (L3)
Resistive Switching Film (L4)
- Electrode (L5)
- Electrode (L3)
Resistive Switching Film (L4)
+ Electrode (L5)
Via (L6)
Via (L6)
Drain/col wire (L7)
NEM Relay Gate (L7)
Src/row wire (L7)
Src
Beam
L1: Vcol routing layer
L2: Vrow routing layer
L3: electrode layer 1
L4: thin film layer
L5: electrode layer 2
L6: row conn. layer
L7: col conn. Layer
Top: vert. NEM relay
…
(Logic circuitry only below here)
Fixup: may be able to route row/col rows together…
Also row wire is touching both electrodes!!!
Src/row wire (L6)
Notes: This is just a draft
Laterally actuated version would have Src/Beam in L7

## Slide 10: Next Steps
Array-level SPICE simulations
GDS layout for single device, different bit widths
Parametrizable layout generator for switch box
Parametrizable layout generator for connection box
Evaluate performance improvements using circuit/arch models