## Slide 1: Hybrid RRAM-NEMS Design for Nonvolatile 3D Routing in CGRAs
Akash Levy

## Slide 2: Designing an application today
Code
CUDA
RTL/HLS
RTL + PNR + Tapeout
CGRA
CGRA*
CGRA
Source: https://hackernoon.com/a-gentle-introduction-to-hardware-accelerated-data-processing-81ac79c2105
* Workload-dependent
Design Flow:
Notes: Today we have many options for designing an application. Here’s a diagram showing the supposed tradeoffs between different application design flows.
Flexibility = What applications can be run on it
Efficiency = EDP
Cost per unit = NRE cost
We have CPUs which you run software on, GPUs which you run CUDA software on, FPGAs which you compile RTL to (or use HLS), and ASICs which have the most complex design flow.
More recently, we also have CGRAs, which are coarse-grained FPGAs, meaning they replace some LUTs with common logic structures. These have a somewhat interesting profile on this scale.
CGRAs are FPGAs that tradeoff a small amount of flexibility for a decent amount of efficiency (depending on workload though)
Same design flow should mean same cost per unit

## Slide 3: How can we improve application design?
Want to improve efficiency without adding cost or reducing flexibility
CGRAs are more efficient than FPGAs b/c less reconfigurable
Low-overhead reconfigurability is key to efficiency with low cost and high flexibility
CGRA is (arguably) best tradeoff b/w flexibility and efficiency at architectural level for agile hardware design
So what else might we do to improve FPGAs/CGRAs?
Notes: Flexibility = agility
Cool… assuming above is true, is that it?
What else can we do? Well basically we want to find a way to reduce reconfigurability overhead.

## Slide 4: Well, where does reconfigurability overhead come from?
LUTs are less efficient than standard cells
  Increase area
  Increases power and delay a little
  Less of a problem for CGRAs: fewer LUTs
Unutilized logic components
  Increase area
  Less of a problem for FPGAs: homogeneity within CLBs
Reconfigurable Routing
  Increases area (80-90% of FPGA area is routing!!!)
  Increases power (5-12x)
  Increases delay (3-4x)
Notes: So we need to think about what causes this overhead. There are three main causes.

## Slide 5: Reducing reconfigurable routing overhead using emerging nanotechnologies
NEM relays:
  Reconfigurable switches monolithically integrated in 3D
  Reduce area/power/delay overhead from reconfigurable interconnects
RRAM:
  Non-volatile memory monolithically integrated in 3D
  Reduce area/power/delay overhead from startup configuration
Result:
  Lower routing overhead
  No startup reconfiguration cost
Notes: Result:
CGRAs become competitive with ASICs in terms of performance
CGRAs become competitive with ASICs for “normally off, instantly on”

## Slide 6: Combining RRAM and NEMS approaches
RRAM and NEM relays have been separately studied for FPGAs
So what is really novel about combining approaches?
KEY POINT: If used together, the electrical properties of RRAM and NEM relays complement each other to cancel essentially all overhead!

## Slide 7: NEM Relays
What are they and how do they work?

## Slide 8
Beam
Source
Drain
Gate
Source
Drain
Gate
Beam
Electrostatic
force
Vpo
Vpi
Vhold
VGS
IDS
Hysteresis Window
Infinite subthreshold slope
3-terminal (3T) NEM relay
OFF-state
ON-state

## Slide 9: 3T & 4T Devices

## Slide 10: Previous work on NEM relays for FPGAs
C. Chen, W. S. Lee, R. Parsa, S. Chong, J. Provine, J. Watt, R. T. Howe, H.-S. P. Wong, and S. Mitra, “Nano-electro-mechanical relays for FPGA routing: Experimental demonstration and a design technique,” in Design, Automation & Test in Europe Conference & Exhibition (DATE), 2012, pp. 1361–1366, IEEE, 2012.
  3D place-and-route scheme with NEM-based LUTs and routers
  Maximum of 41.9% performance gain
  Assumed multiple NEMS devices can be viably stacked in 3D (not yet!)
C. Chen, R. Parsa, N. Patil, S. Chong, K. Akarvardar, J. Provine, D. Lewis, J. Watt, R. T. Howe, H.-S. P. Wong, et al., “Efficient FPGAs using nanoelectromechanical relays,” in Proceedings of the 18th annual ACM/SIGDA international symposium on Field programmable gate arrays, pp. 273–282, ACM, 2010.
  Half-select programming scheme was used for the NEM relays, verified expt.
  Claimed 10-fold reduction in leakage power, 2-fold reduction in dynamic power, and 2-fold reduction in area
  Use of a 3T device and a small hysteresis window: bad for pass transistor
  Used optimistic device parameters/dimensions… not realized physically

## Slide 11: Half-Select Design for NEM Relay R/W

## Slide 12: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties |  | 
Infinite subthreshold slope | Storage is volatile |  | 
Lower ON-state resistance than transistors | Larger than transistors |  | 
Hysteresis enables data storage | Much slower switching than transistors |  | 
3D integration | Higher Vg req. than CMOS |  | 
No leakage current |  |  | 

## Slide 13: RRAM
What is it and how does it work?

## Slide 14
Bottom Electrode
Resistive Switching Film
Top Electrode
=
Bipolar RRAM Cell
Many possible materials for resistive switching film
Many possible R/W circuit architectures
Key properties:
  Endurance
  Retention
  Max DC current/voltage
  LRS, HRS, resistance ratio
  DC peak voltage
Publication & Year | VLSI 2014 | VLSI 2014 | IEDM 2014 | IEDM 2014 | VLSI 2015 | VLSI 2015
2D/3D Geometry | 2D Planar | 3D Vertical | 2D Planar | 3D Vertical | 2D Planar | 2D Planar
Switch Type | Bi | Bi | Bi | Bi | N/A | Bi
Structure | 1T-1R | 1R | 1T-1R | 1R | 1T-1R | 1R
TE/material/BE | Al/AlOx/WOx/W | TiN/HfOx/TiN | TiN/Ti/HfO2/TiN | Pt/HfOx/TiN | Ir/Ta2O5/TaOx/TaN | TiN/TiO2/a-Si/TiN
Cell Area (μm2) | 0.0324 (.18um) | 0.000003 | 0.01 (100nm) | 1 (15nm) | 0.0016(40nm) | 0.0013
Speed [ns] | ~1000 | 50 | 40 | 20 | N/A | 10
DC Peak Voltage [V] | N/A | <3 | <3 | <2.5 | N/A | 6.5
DC Peak Current [uA] | N/A | ~500 | ~60 | ~100 | N/A | 5
HRS/LRS Ratio | >180 | >10 | 10 | 100 | 10 | 10
R high [Ω] | 3x107 | 106 | 2x105 | 3x107 | 5x104 | 108
R low [Ω] | 3x104 | 104 | 2x104 | 3x104 | 4x103 | 107
Endurance | 109 | 104 | 103 | 108 | >105 | 106
Retention | 10y@ 85℃ | 20000h@ 250℃ | 10y@ 70℃ | 10y@ RT | 10y @ 85℃ | 3y @ 55℃
VRESET
VSET
V
I
SET
HRS
LRS
RESET
Compliance

## Slide 15: Previous work on RRAM relays for FPGAs
Y. Y. Liauw, Z. Zhang, W. Kim, A. El Gamal, and S. S. Wong, “Nonvolatile 3D-FPGA with monolithically stacked RRAM-based configuration memory,” in Solid-State Circuits Conference Digest of Technical Papers (ISSCC), 2012 IEEE International, pp. 406–408, IEEE, 2012.
  1T2R structure with two RRAM cells having opposite resistance states
  Voltage divider controlling a pass transistor
  Experimentally achieved a 57% smaller die area and a 28% lower energy-delay-product (EDP) than SRAM-based design
  Non-volatile configuration memory which enabled quick wake-up

## Slide 16: RRAM 1T2R Operation Modes

## Slide 17: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties | Good properties | Bad properties
Infinite subthreshold slope | Storage is volatile | Nonvolatile | Large write energy
Lower ON-state resistance than transistors | Larger than transistors | Lower area than SRAM and proven scalable | Sense amp to decode takes up area
Hysteresis enables data storage | Much slower switching than transistors | Resistance-based storage allows analog design | 
3D integration | Higher Vg req. than CMOS | 3D integration | 
No leakage current |  |  | 

## Slide 18: How can we synergize RRAM & NEM relays?
KEY IDEA: use RRAM to control gate voltage of NEM relays for actuation
More generally: NEM relays are an interesting option for RRAM sense amplification, given their infinite subthreshold slope
NEM relays have better electrical characteristics than pass transistors

## Slide 19
Mode | Param | Value
COPY | Vrow | 
 | Vcol | 
HOLD | Vrow | 
 | Vcol | 
SET | Vrow | 
 | Vcol | 
RESET | Vrow | 
 | Vcol | 
Mode | Param | Value
COPY | Vrow | 
 | Vcol | 
HOLD | Vrow | 
 | Vcol | 
SET | Vrow | 
 | Vcol | 
RESET | Vrow | 
 | Vcol | 
(b)
Hybrid circuit architecture
(b)
out
Vg
Vcol,1
Vcol,2
in1,1
in1,2
in2,1
in2,2
Vrow,1
Vrow,2
out1,1
out1,2
out2,1
out2,2
Hysteretic 3T NEM Router
RRAM Cell
Thin Film Resistor (TFR)
(a)
Vg
R1
Notes: Key idea: use RRAM to actuate the NEM relays
Entirely back-end-of-line (0T)
1N1R design
Need a good way to actuate
Poly layers are annoying to get to
RRAM properties have to match NEM relays’

## Slide 20
COPY
HOLD
OFF
SET
OFF
COPY
HOLD
OFF
RESET
OFF
COPY
HOLD

## Slide 21: Row/col controllers
Mux
VCOPY
VHOLD
4:1 Decoder
V’SET
V’RESET
Row
Mode
2
2
== COPY or HOLD
Vrow
NEM Relay/
PU Transistor
Vrow,1
Vrow,2
Vrow,3
Vrow,4
NEM Relay/
PU Transistor
NEM Relay/
PU Transistor
NEM Relay/
PU Transistor
4:1 Decoder
Col
Mode
2
2
== COPY
NEM Relay
NEM Relay
NEM Relay
NEM Relay
Vcol,1
Vcol,2
Vcol,3
Vcol,4
NEM Relay/
PD Transistor
NEM Relay/
PD Transistor
NEM Relay/
PD Transistor
NEM Relay/
PD Transistor
(a)
(b)
!= HOLD
Notes: (single stream for reduced I/O pin requirement)
Probably want to do this on-chip to reduce pin requirement
Column controller is similar

## Slide 22: Properties that lead to overhead cancellation
NEM Relays |  | RRAM | 
Good properties | Bad properties | Good properties | Bad properties
Infinite subthreshold slope | Storage is volatile | Nonvolatile | Large write energy
Lower ON-state resistance than transistors | Larger than transistors | Lower area than SRAM and proven scalable | Sense amp to decode takes up area
Hysteresis enables data storage | Much slower switching than transistors | Resistance-based storage allows analog design | 
3D integration | Higher Vg req. than CMOS | 3D integration | 
No leakage current |  |  | 
Bad Material Property | Good Material/App Property that Cancels It
NEM relays: much slower switching than transistors | Used for routing only: only switches once on startup, hysteresis enables dual function as memory and router
NEM relays: larger than transistors | Used for routing only and integrated in 3D
NEM relays: storage using hysteresis is volatile | RRAM is nonvolatile: integration enables nonvolatility
NEM relays: higher Vg required than CMOS | RRAM variable resistance allows analog control of Vg
RRAM: larger write energy | RRAM is used as ROM
RRAM: sense amp to decode takes up area | NEM relays have infinite subthreshold slope, so single relay can act as decoder
RESULT: Architecture is entirely free of transistors, so can be implemented 100% in BEOL i.e. 3D

## Slide 23: Island-Style Architecture
CB
CLB
CB
SB
One CGRA Tile
Source: FPGA Architectures: An Overview - Springer
Notes: CLB: configurable logic block
CB: connection box
SB: switch box

## Slide 24: Connection boxes
CLB
CLB
Fc = 0.5

## Slide 25: RRAM/NEMS switch BEOL standard cell layout
Vcol wire (L1)
Vrow wire (L2)
Via (L2)
Vrow wire (L2)
+ Electrode (L3)
Resistive Switching Film (L4)
- Electrode (L5)
- Electrode (L3)
Resistive Switching Film (L4)
+ Electrode (L5)
Via (L6)
Via (L6)
Drain/col wire (L7)
NEM Relay Gate (L7)
Src/row wire (L7)
Src
Beam
L1: Vcol routing layer
L2: Vrow routing layer
L3: electrode layer 1
L4: thin film layer
L5: electrode layer 2
L6: row conn. layer
L7: col conn. Layer
Top: vert. NEM relay
…
(Logic circuitry only below here)
Fixup: may be able to route row/col rows together…
Also row wire is touching both electrodes!!!
Src/row wire (L6)
Notes: This is just a draft
Laterally actuated version would have Src/Beam in L7

## Slide 26: Switch boxes
Source: http://venividiwiki.ee.virginia.edu/mediawiki/index.php/File:SwitchBo.png
Flexibility: Fs = 3

## Slide 27: Layout strategy: 3D fold
CLB
CLB
CLB
CLB
CB
SB
SB
CB
SB
CB
SB
SB
CB
SB
CB
SB
SB
CB
CB
CB
SB
CB
CB
CB
CB
CB
CLB
CB
SB
CB
CLB
CB
SB
CB
CLB
CB
SB
CB
CLB
CB
SB
Ideal…
Notes: Need to get to 1/3 area for full utilization

## Slide 28: Device Constraints
0
Hysteresis Window
Vpo,min
Vpo,max
Vpi,min
Vpi,max
VH,min
VH,max
VSET,min
VSET,max
VN,max
VL,max
-VH,max
VRST,min
VRST,max
-VN,max
…
RRAM Voltage Control

## Slide 29: Next Steps
Understand architectural options for voltage divider better
GDS layout for single device
Parametrizable layout generator for switch box
Parametrizable layout generator for connection box
Evaluate performance improvements using circuit/arch models
Future projects:
  Apply architecture to LUTs
  Fabricate RRAM-actuated NEM relay

## Slide 30: Future Work: LUTs with RRAM/NEMS
Source: FPGA Architectures: An Overview - Springer
Notes: Ultimately you want all static configuration to use this architecture

## Slide 31
Beam
Source
Drain 1
Drain 2
Gate
Source
Drain 1
Drain 2
Gate
Beam
Electrostatic
force
Vpo
Vpi
Vhold
VGS
ID1S
Vpo
Vpi
Vhold
VGS
ID2S

## Slide 32: Summary
RRAM and NEM relays work well together for reconfigurable routing
100% BEOL design enables isolation of layout for routing and logic
That’s all, folks!
Area Improvements | Power Improvements | Delay Improvements
Routing components in 3D | Lower ON-state resistance | Lower ON-state resistance
Routing components require fewer elements | Low-power startup with integrated NVM | Fast startup with integrated NVM
No config registers/SRAM | Shorter wire lengths | Shorter wire lengths
 | No leakage current | 

## Slide 33
Bottom Electrode
Resistive Switching Film
Top Electrode
=
VRESET
VSET
V
I
SET
HRS
LRS
RESET
Compliance
(a)
(b)